## Slide 1: Design optimization for HPC using FPGA
Murat Isik, Kayode Inadagbo ,Hakan Aktas Annual International Conference on Information Management and Big Data, 142-156 2023

## Slide 2: Goal of the paper
This research paper focuses on :
  Optimizing Field Programmable Gate Arrays (FPGAs) for high-performance computing (HPC) in machine learning (ML) inference tasks.
  How to improve the performance of an open-source inference accelerator using various optimization techniques.

## Slide 3: Paper outlines
Introduction
Methodology - Optimizing FPGA Performance
Baseline design Dual clock solution Ultra RAM solution Compiler Strategy with large local memory
Conclusions
References
Motivation
Open-source ML inference accelerator
Results

## Slide 4: Introduction
This research explores how Field-Programmable Gate Arrays (FPGAs) can be optimized for high-performance computing (HPC), particularly in machine learning (ML) inference tasks.
FPGAs offer a unique combination of flexibility, parallel processing, and energy efficiency, making them suitable for real-time data processing.
FPGAs are not widely used in HPC due to challenges like complex programming, memory limitations, and optimization difficulties.

## Slide 5: GOAL
Optimizing Tensil AI’s open-source inference accelerator to improve ML inference performance.
The goal is to achieve high inference speed while maintaining accuracy and energy efficiency.

## Slide 6
Motivation
FPGAs have unique advantages:
  High Parallelism: FPGAs can perform many tasks in parallel, which is crucial for applications like image processing and machine learning.
  Customizable Architecture: FPGAs can be programmed to meet specific performance needs, unlike general-purpose processors.
  Low Latency: FPGAs can process data in nanoseconds, making them ideal for real-time applications.
  Energy Efficiency: FPGAs consume less power compared to CPUs and GPUs, which is important for applications that require high processing power but have limited energy resources.

## Slide 7
Motivation
FPGAs challenges in HPC:
  Complex programming : Requires expertise in hardware description languages ( VHDL , Verilog .. ).
  Limited on-chip memory: Leads to frequent data transfer between the FPGA and external memory.
  Floating-point limitations : FPGAs typically use fixed-point arithmetic, which may slightly reduce accuracy.
  Development cost and complexity : FPGA tools are expensive and require specialized knowledge.

## Slide 8: Open-Source ML Inference Accelerators
Machine Learning (ML) inference: is using a trained model to make predictions on new data , in this paper “ResNet20” used .
Open-source ML inference accelerator : is used to provide efficient and customizable solutions for running ML models on hardware like FPGAs , in this paper “Tensil AI” used.
Specialized ML inference accelerators improve speed, power efficiency, and cost-effectiveness.

## Slide 9: Open-Source ML Inference Accelerators
VTA (Versatile Tensor Accelerator) : an open-source ML inference accelerator performs tasks with the help of a highly optimized hardware accelerator.
TensorFlow, PyTorch, and ONNX are among the popular ML frameworks supported by VTA .
There are many hardware platforms can be used with VTA, including FPGAs and ASICs.

## Slide 10: Open-Source ML Inference Accelerators
Tensil AI's accelerator key features :
  Quantization : Converts floating-point models into lower-precision representations to reduce power consumption and memory usage.
  Dynamic shape support : Can process inputs of varying sizes and shapes efficiently.
  High configurability : Can be adjusted for different applications.

## Slide 11: Methodology - Optimizing FPGA Performance
Four key optimization strategies inderduced to techniques to improve the performance of ResNet20 model on Xilinx ZCU104 FPGA board.
Baseline design.
Dual clock solution.
Ultra RAM solution.
Compiler Strategy with large local memory.

## Slide 12: Methodology - Baseline design
The ResNet20 model is trained using CIFAR-10.
The trained model is tested on an FPGA using a 32 × 32 systolic array (a hardware architecture optimized for matrix operations).
The FPGA is clocked at 100MHz, and Block RAM (BRAM) is used for memory storage.
Results:
  133.54 FPS (frames per second )
  90% accuracy (compared to 92% in TensorFlow)
  Accuracy drop is due to the conversion from 32-bit floating-point to 16-bit fixed-point representation.

## Slide 13: Methodology - dual-clock
The FPGA is clocked at 100MHz, but data transfer bottlenecks reduce performance.
Solution: Introduce a dual-clock domain:
Compute part (Tensil AI block) stays at 100MHz.
Memory interface (ZYNQ block) runs at 333MHz, improving data movement.
Results:
  152.04 FPS (compared to 133.54).
  Faster memory access improves inference speed.

## Slide 14: Methodology - Ultra RAM
Limited on-chip memory forces frequent reloading and slowing performance.
Solution: Use Ultra RAM (URAM) in addition to Block RAM:
Ultra RAM provides higher memory density and faster access than standard BRAM.
Reduces the need to reload data multiple times.
Results:
  FPS increased to 170.16
  Larger memory allows processing larger chunks of the network at once.

## Slide 15: Methodology - Compiler Strategy
Traditional compilers assume that models are too large to fit into FPGA memory.
Solution: Modify the compiler to optimize data placement:
Store weights and activations in local memory instead of reloading them repeatedly.
Reduces memory access latency and speeds up processing.
Results:
FPS final value: 290.58 FPS

## Slide 16: Results – Performance Comparison
Technology | Frequency | Power (W) | FPS | Throughput (GOP/s) | Energy Efficiency (GOP/s/W)
Intel Xeon E5-2697 (CPU) | 2300MHz | 145W | 11.37 | 37.62 | 0.19
NVIDIA GTX 1080 Ti (GPU) | 1481MHz | 250W | 6.15 | 235.77 | 0.94
Tensil AI on FPGA | 100MHz | 5.21W | 290.58 | 21.12 | 4.05

## Slide 17: Results – Performance Comparison
FPGA solution is 4.05 times more energy efficient than a CPU .
FPGA solution is 4x faster than the GPU.
GPU and CPU consume significantly more power than FPGA-based inference.

## Slide 18: Conclusion
The research successfully improves ML inference performance on FPGAs by:
  Using a dual-clock system for faster memory transfers.
  Leveraging Ultra RAM to minimize data reloading.
  Optimizing compiler strategies to store data efficiently.

## Slide 19: Conclusion
FPGA-based acceleration is highly effective for machine learning tasks, offering a balance between performance, accuracy, and energy efficiency.
Significant improvements in frame rate and energy efficiency by optimizing the hardware design, using Ultra RAM, and employing advanced compiler strategies.
Future work includes exploring Dynamic Partial Reconfiguration, a technique that allows parts of the FPGA to be reconfigured at runtime, which could further improve performance and flexibility.

## Slide 20: Comparison
comparing the proposed FPGA-based implementation with previous implementations
Work | Device | Frequency (MHz) | Quantization | Power (W) | FPS (Frames Per Second) | Throughput (GOP/s) | Energy Efficiency (GOP/s/W)
Ma et al. [22] | Arria-10 GX | 150 | 8-16 bit fixed | 21.2 | - | 645.25 | 30.44
Mei et al. [23] | Virtex-7 | 200 | 16-bit floating | 10.81 | 6.58 | 202.42 | 1.64
Zhang et al. [24] | Zynq ZU7EV | 300 | 8-bit fixed | 17.67 | - | 290.40 | 0.80
Blott et al. [25] | Zynq ZU3EG | 220 | 8-bit fixed | 10.2 | 200 | 400 | 39.21
Zhang et al. [26] | Virtex-7 | 200 | 8-bit fixed | 6.32 | 6.77 | 209.60 | 33.16
Li et al. [27] | Zynq 7010 | 200 | 16-bit fixed | 19.52 | - | 452.8 | 23.20
Suda et al. [28] | Stratix-V | 120 | 8-16 bit fixed | 25.8 | - | 117.8 | 4.56
(This Paper) | Zynq ZU7EV | 100 | 32-bit floating | 5.21 | 290.58 | 21.12 | 4.05

## Slide 21: References
Wang, H. et al. (2019). Convolutional neural network accelerator on FPGA. IEEE ICTA.
Vanderbauwhede, W., Benkrid, K. (2013). High-Performance Computing Using FPGAs. Springer.
Blaiech, A.G. et al. (2019). Survey on FPGA-based deep learning accelerators. J. Syst. Archit.
Zou, D. et al. (2013). High-performance sparse matrix-vector multiplication on FPGA. IEICE Electron. Express.
Isik, M. et al. (2023). Energy-efficient reconfigurable autoencoder implementation on FPGA. arXiv.
Woods, R. et al. (2008). FPGA-based Implementation of Signal Processing Systems. John Wiley & Sons.
Tensil AI Website (Accessed: 2022-12-17). https://www.tensil.ai.
Tensil AI GitHub (Accessed: 2022-12-17). https://github.com/tensil-ai.
Sundararajan, P. (2010). High-performance computing using FPGAs. Citeseer.
Sklyarov, V. et al. (2019). Hardware accelerators for high-performance computing. Int. J. Innov. Comput.
Huang, S. et al. (2019). Accelerating sparse deep neural networks on FPGAs. IEEE HPEC.
Chen, Z. et al. (2022). FPGA-based in-vivo calcium image decoding. arXiv.
Kohda, S., Yoshida, K. (2021). Characteristics of high-frequency trading. IEEE COMPSAC.
Karandikar, S. et al. (2019). Using FireSim for FPGA system simulation.
Moreau, T. et al. (2019). Hardware-software blueprint for deep learning. IEEE Micro.
Zunin, V. (2021). Intel OpenVINO toolkit for object detection. IEEE RusAutoCon.
Xilinx Deep Learning Processor Unit (DPU) Docs (Accessed: 2022-12-17).
Morcos, B. (2019). NengoFPGA: A backend for the Nengo neural simulator. Univ. of Waterloo.
DeWolf, T. et al. (2020). Low-power AI hardware for neurorobotics. Front. Neurorobotics.
Gosmann, J., Eliasmith, C. (2017). Optimization in Nengo neural network simulator. Front. Neuroinformatics.
Ma, Y. et al. (2017). Optimizing loop operation for FPGA acceleration of CNNs. ACM FPGA.
Mei, C. et al. (2017). VGG16 FPGA accelerator on Xilinx VX690T. IEEE GlobalSIP.
Zhang, M. et al. (2019). Optimized compression for CNNs on FPGA. Electronics.
Blott, M. et al. (2018). FINN-R: Deep-learning framework for quantized NN exploration. ACM TRETS.
Zhang, X. et al. (2020). FPGA-based quantized image classification. Electronics.
Li, L. et al. (2019). Efficient object detection for remote sensing images. Remote Sensing.
Suda, N. et al. (2016). Optimized OpenCL-based FPGA accelerator for CNNs. ACM FPGA.

## Slide 22: Thank you
Abdullah Alasmari
446811106